Experimental Rocket Fuel

Fuel Test One
Fuel/Oxy
fuel: Gasoline, Polystyrene
oxy: N/A
ratio: Enough Gasoline to thicken Polysyrene, no specific ratio used
Mold:
mold: 1"x12" PVC
data formed: 8/14
date removed: N/A
Notes:
Abandoned due to the fact that the gain formed an airtight seal in the PVC pipe keeping the bottom 90% from drying

Fuel Test Two
Fuel/Oxy
fuel: Gasoline, Polystyrene
oxy: Gaseous Oxygen
ratio: Enough Gasoline to thicken Polysyrene, no specific ratio used
Mold:
mold: flattened using roller until about 5mm thick, a day later, was rolled into tube
data formed: 8/26
date removed: 8/29
Notes:
Fuel grain burnt! Need much more oxy for the grain to burn inside out and for more combustion inside the combustion chamber