Rocket Static Test Preparation Checklist

- General Tasks
  - Preparation Meeting
    - Everyone is informed of engine information
    - Everyone is informed of general safety
    - Everyone is informed of roles
      - Test Director (General tasks)
      - Data Collection
      - Engine
      - Safety
      - Photography
    - Have fun, but don’t be and idiot
  - Table for equipment
  - Power available
  - Lights are properly mounted
- Data Collection
  - Video cameras setup
    - #1 Mounted on tripod behind engine
    - confirm free-space in camera storage
    - #2 Mounted on engine test stand
    - confirm free-space in camera storage
  - Sensors connected to engine
  - Sensor cable ran from engine to computer
  - Sensors connected to MCU
  - MCU connected to computer
  - Start data collection software
    - Zero load cell
    - Confirm force is at 0N
    - Confirm accuracy of temperature sensors
- Engine
  - Confirm all connections are tight and mounted properly
    - Fuel inlet
    - Oxygen inlet
    - Injector
    - Chamber
    - Nozzle
  - Fuel line connected to engine
  - Oxygen line connected to engine
  - Run fuel and oxygen lines from engine to tanks
  - Ensure fuel tank valve is closed
  - Connect fuel line to fuel tank
  - Ensure oxygen tank valve is closed and regulator is set properly
  - Connect oxygen line to oxygen regulator
- Safety
  - Everyone wearing safety glasses
  - Fire extinguisher on hand
  - Water supply available
  - cables bundled/taped down
  - Blast shield integrity confirmed
- Photography
  - Photographs of team
  - Photograph of EVERYTHING!